## Slide 1: Welcome to the World of Assembly Language Programming
Base Slide Prepared by Madhusudan Basak
Lecturer Department of CSE, BUET
Modified by
Abdus Salam Azad, Assistant Professor, CSE, BUET

## Slide 2: References
Assembly Language Programming and Organization of the IBM PC
--- Ytha Yu and Charles Marut
Assembly Language for the IBM-PC
--- Kip R. Irvine

## Slide 3: What Is Assembly Language ?

## Slide 4: Definition (Simplified) from wiki
a low-level programming language for a computer, in which there is a very strong (generally one-to-one) correspondence between the language and the architecture's machine code instructions.
  Each assembly language is specific to a particular computer architecture --- Platform Dependent

## Slide 5: Why use it ?
Direct hardware manipulation
  Gives you complete control over the system's resources
Performance and efficiency
Access to specialized processor instructions

## Slide 6: Disadvantages 
Hard and tedious
Non-portable(machine dependent)
Bug-prone
Difficult to debug

## Slide 7: A question ?
In what kind of situations, assembly language will be the only/best solution?
Drivers and communication with custom hardware/electronics.
An Compiler
Optimizations

## Slide 8: Chapter 1 Microcomputer Systems

## Slide 9: The Components of a Microcomputer System
Functionally three parts
  CPU
  Memory circuits
  I/O circuits

## Slide 10: Bus
A set of wires or connections with which a processor communicates with memory and l/O circuits
There are three kind of buses:
  address bus
  data bus,
  control bus

## Slide 11: Bus Connections

## Slide 12: Memory - Bytes and Words

## Slide 13: CPU
Two main components
  Execution Unit(EU)
  Bus Interface Unit(BIU)

## Slide 14: Intel 8086 Microprocessor Organization

## Slide 15: Execution Unit
The purpose of the execution unit (EU} is to execute Instructions.
  It contains a circuit called the arithmetic and logic unit (ALU).
    The ALU can perform arithmetic (+, - , x ,I) and logic (AND, OR, NOT} operations.
The data for the operations are stored in registers
A register is like a memory location except that we normally refer to it by a name rather than a number.
The EU has eight registers for storing data; their names arc AX, BX, CX, DX, SI, DI, BP, and SP.

## Slide 16: Bus Interface Unit
The Bus Interface unit (BIU) facilitates communication between the EU and the memory or I/0 circuits.
It is responsible for transmitting addresses, data, and control signals on the buses.
Its registers are named CS, DS, ES, SS, and IP.
  They hold addresses of memory locations.
  The IP (instruction pointer) contains the address of the next instruction to be executed by the EU.

## Slide 17: Instruction Execution
Fetch
  Fetch an instruction from memory.
  Decode the instruction to determine the operation.
  Fetch data from memory if necessary.
Execute
  4. Perform the operation on the data.
  5. Store the result in memory if needed

## Slide 18: Organization of the ibm personal computers
Chapter 3

## Slide 19: Organization of the 8086/8088 Microprocessors
Registers
  There are fourteen 16 bit registers
  3 Types of registers
    Data Registers – holds data for operation
    Address Registers – holds addresses of instruction or data
    Status Register – holds current status of processor

## Slide 20: Data Registers
AX (Accumulator Register)
BX (Base Register)
CX (Count Register)
DX (Data Register)
Each one can be used by parts
  e.g., AX has two equal parts
    The higher part (8 bit) is referred as AH and
    The lower part – AL
    both of them can be used independently

## Slide 21: Data Registers

## Slide 22: Memory Organization
8086 features 1 20 bit physical address for memory
  2^20 == 1MB Memory is supported
However, all registers are of 16 bit
The memory is divided (non-disjoint) into segments

## Slide 23: Segment
Each segment consists of a block of 2^16 consecutive bytes in the memory
  64KB in size
  Each memory location in a memory segment is addressable by a 16 bit offset
Each segment is identified with a 16 bit segment number
  Hence there are 2^16 segments
  Numbered from 0000h to FFFFh

## Slide 24: Logical Address and Physical Address
Each Location in memory can be addressed by specifying a segment number and and offset within the segment
  Written as segment:offset
  Called the logical address
To find the physical address from a logical address
  Shift left the segment number by four bit, then add offset
  segment*10h + offset

## Slide 25
If you have a segment A4FBh and offset 4872h. Then what is the 20 bit physical address?
    A4FB0h
    +4872h
    -------------
    A9822h ( 20 bit physical address)

## Slide 26: Segment Registers(Address Registers)

## Slide 27: Pointer and Index Registers, Instruction pointers (Address Registers)

## Slide 28: Overlapping Scenario

## Slide 29: Overlapping Scenario

## Slide 30: Physical and Logical address calculation

## Slide 31: Segment Registers
Code, Data, and Stack are maintained in different segments
Stack is used by the processor to implement procedure calls.
Task | Segment Registers | Pointer and Index Registers
Code | CS | IP
Data | DS | SI
 | ES | EI
Stack | SS | SP
 |  | BP

## Slide 32: FLAGS Register(Status Register)

## Slide 33: Memory Organization of the PC
8086/8088 has only 1MB of memory
Not all memory for application programs
Interrupt Vector, Video Display Memory etc are needed
IBM fixed all the positions and allowed all to live happily

## Slide 36: I/O ports addresses
The 8086/8088 supports· 64 KB of I/0 ports
Interrupt controller (20h-21h)
Keyboard controller (60h-63h)
etc...