## Slide 1: CHAPTER 9 Multiplication and Division Instructions

## Slide 2: Signed Vs Unsigned Multiplication
Signed and Unsigned numbers must be interpreted accordingly
P = 10000000 * 11111111
Unsigned Interpretation
  P = 128 * 255 = 32640
Signed Interpretation
  P = -128 * -1 = 128
Hence
  P = 0111111110000000b ; unsigned multiplication
  P = 0000000010000000b ; signed multiplication
PRODUCT IS DIFFERENT with respect to INTERPRETATION ( for numbers that are negative )

## Slide 3: Multiplication instructions
imul source
  Signed multiply [Integer MULtiply]
mul source
  Unsigned multiply
Byte and Word Multiplication (A X B)
  If two bytes are multiplied, the result is a 16-bit word
    A: source
    B: AL
    product: AX
  If two words are multiplied, the result is a 32-bit doubleword
    A: source
    B: AX
    Product: DX:AX
      Product (ms 16 bits): DX
      Product (ls 16 bits): AX

## Slide 4: Multiplication instructions
source can be a register or memory byte/word, but can not be a constant
Byte form
  AX=AL*source
Word form
  DX:AX=AX*source
CF/OF
  MUL
    0: upper half of result is 0
  IMUL
    0: if upper half is sign extension of lower half.
  CF/OF = 1 means product is too big for lower half of the destination (AL for byte and AX for word)
If ax contains 0001h and bx contains FFFFh
  mul bx; dx = 0000h ax = FFFFh
  imul bx ; dx = FFFFh ax = FFFFh (-1)
SF, ZF, AF, and PF
  Undefined

## Slide 5: More Examples
Instruction | Hex Product | DX | AX | CF/OF
MUL BX | FFFE0001 (4294836225) | FFFE (!zero) | 0001 | 1
IMUL BX | 1 | 0000 | 0001 | 0
AX=FFFFh,BX=FFFFh
AX=80h,BX=FFh
Instruction | Hex Product | AH | AL | CF/OF
MUL BX | 7F80 (128) | 7F(!zero) | 80 | 1
IMUL BX | 0080 | 00 (no sign extension) | 80 | 1

## Slide 6: Division instructions
cbw
  convert byte to word
cwd
  convert word to doubleword
div source
  unsigned divide
idiv source
  signed divide

## Slide 7: Byte and Word Division (A/B)
When division is performed
  two results: the quotient and the remainder
  Quotient and remainder are the same size as the divisor
  Divisor can not be a constant

## Slide 8: Byte and Word Division (A/B) (contd.)
For the byte form,
  Divisor, B: source ;Dividend , A: AX
  Quotient : AL ;Remainder: AH
  AL = AX / divisor; divisor is BYTE
  AH = AX % divisor;
For the word form,
  Divisor, B: source ;Dividend , A: DX:AX
  Quotient: AX ; Remainder: DX
  AX = DX:AX / divisor ; divisor is WORD
  DX = DX:AX % divisor

## Slide 9: An Example
;If dx = 0000h, ax = 0005h, and
bx = FFFEh (-2)
div bx; ax = 0000h dx = 0005h
idiv bx; ax = FFFEh dx = 0001h

## Slide 10: Divide Overflow
It is possible that the quotient will be too big to fit in the specified destination (al or ax)
if the divisor is much smaller than the dividend
the program terminates and the system displays the message "Divide Overflow"

## Slide 11: Sign Extension of the Dividend
Word division
  The dividend is in dx:ax even if the actual dividend will fit in ax
  For div, dx should be cleared
  For idiv, dx should be made the sign extension of ax using cwd
e.g. -1250/7
MOV AX,-1250
CWD ; sign extend
MOV BX,7
IDIV BX

## Slide 12: Sign Extension of the Dividend
Byte division
  The dividend is in ax even if the actual dividend will fit in al
  For div, ah should be cleared
  For idiv, ah should be made the sign extension of al using cbw

## Slide 13: Thank You